## Slide 1: Static Detection of Packet Injection Vulnerabilities --- A Case for Identifying Attacker-controlled Implicit Information Leaks
Qi Alfred Chen, Zhiyun Qian†, Yunhan Jack Jia, Yuru Shao, Z. Morley Mao
University of Michigan, †University of California - Riverside

## Slide 2: Packet injection attack
Inject attack packet into an existing communication channel (TCP, RTP, etc.)
  Attacker is off-path: more realistic than MitM
TCP
HTTP
Inject spoofed pkt
Phishing
Javascript
injection
XSS,
CSRF
Off-path attacker

## Slide 3: Packet injection attack
HTTP
Application layer encryption
  Low coverage (only 30%)
  1st HTTP request vulnerable to hijack [Qian, CCS’12]
  Vulnerable to DoS
TCP
HTTPS
Hijack
Phishing
Javascript
injection
XSS,
CSRF
Inject spoofed pkt
Off-path attacker
is limited

## Slide 4: Packet injection attack
HTTP
Application layer encryption
  Low coverage (only 30%)
  1st HTTP request vulnerable to hijack [Qian, CCS’12]
  Vulnerable to DoS
TCP
HTTPS
RST
is limited

## Slide 5: Current countermeasures
To combat such threat, typically stringent checks are used
  E.g., RFC 5961 for blind in-window TCP attacks
However, even if design is secure, the actual implementation may not always conform to it
  TCP code in Linux & FreeBSD found to be much weaker than RFC1
  Windows-specific implementation enables fast sequence number cracking2
Calls for a systematic approach to verify network protocol implementations
1Qian et al., CCS’12
2Gilad et al., WOOT’12

## Slide 6: Our solution: PacketGuardian
An effective and scalable static analysis tool
  Systematically evaluate robustness of a protocol implementation against such attacks
For high effectiveness,
  Support precise context, flow, field-sensitive taint analysis with pointer analysis
  Support implicit flow analysis
  The first to propose and detect attacker-controlled implicit information leaks
For high scalability,
  Choose summary-based approach

## Slide 7: Our solution: PacketGuardian
Requires access to source code
  A realistic assumption for many key protocols
Applied to 6 real protocol implementations
  Covering TCP, RTP, SCTP, etc.
  Discovered a set of vulnerabilities not previously reported

## Slide 8: An illustrative example
Entry point
  Handle incoming packets
Packet acceptance point
  Copy payload to upper layer
  Terminate the channel
Accept paths
If any accept paths is weak, a vulnerability is directly revealed
Handle_incoming_pkt(pkt)
accept_pkt()
Check pkt.f2
Check pkt.f1
Check pkt.f3
Check pkt.f1
pkt.f1 == 100?

## Slide 9: An illustrative example
If all accept paths have strong checks
  Usually protected by protocol states that are hard to guess
A further question: will the protocol state be leaked to attacker?
  All recent TCP packet injection vulnerabilities exploit this!
Handle_incoming_pkt(pkt)
accept_pkt()
Check pkt.f1
Check pkt.f3
pkt.seq in win1 around rcv_nxt?
pkt.ack in win2 around snd_nxt?
232
232

## Slide 10: An illustrative example
If all accept paths have strong checks
  Usually protected by protocol states that are hard to guess
A further question: will the protocol state be leaked to attacker?
  All recent TCP packet injection vulnerabilities exploit this!
(pkt.seq > rcv_nxt)?
Trigger public event, e.g., a storage channel
Collaborative attacker
Y
N
Bigger? Smaller?
Binary search
rcv_nxt
Crack TCP sequence number under 1 sec!

## Slide 11: A new class of implicit information leaks
A unique implicit information leak
  Attacker data involved
Classic implicit flow leaks
  Low exploitability
SCD1 based leaks
  High exploitability
(pkt.seq > rcv_nxt)?
Trigger public event, e.g., a storage channel
Y
N
(attack_data > secret)?
(secret == Const)?
Side-channel leaks in web/
Android apps
Crypto key extraction (e.g., in cloud)
1Bao et al., ISSTA’10
1
0
1
1
Collaborative attacker
A new class of highly-exploitable implicit information leaks!
Call it “attacker-controlled implicit information leaks”
We are the first to propose and design a tool to detect it

## Slide 12: PacketGuardian design overview
Accept path constructor
Static taint analysis
Vulnerability analyzer
Weak
accept paths
Protocol states
Highly-vulnerable
leakage
paths
Packet injection Vulnerabilities
Patch 1
Patch 2
Patch 3
Prioritize attacker-
controlled implicit information leaks
Leak path constructor

## Slide 13: Static taint analysis
Taint engine
  High precision: flow, field, context sensitive
  Pointer analysis
  Implicit flow tracking
    Commonly excluded
Summary-based approach
  High scalability
  Callee-to-caller order
    Lower complexity
  Makes taint path construction unnatural
    Solved by bookkeeping taint path info in path & tracking summary
Static taint analysis
Taint engine
SCC
generator
Pointer analysis
Function summary
SCC
- Taint
- Pointer
- Tracking
- Path

## Slide 14: Vulnerability analyzer
Static taint analysis
Taint engine
Pointer analysis
- Taint
- Pointer
- Tracking
- Path
Function summary
Accept path constructor
Vulnerability analyzer
Leak path constructor
Weak
accept paths
Highly-vulnerable
leakage
paths
Packet injection Vulnerabilities
Protocol states
Accept path constructor
SCC
generator
SCC

## Slide 15: Accept path analysis
Taint source:
  Attack-controlled data
Taint sink:
  Packet accept function
Path & tracking summary
Path pruning to reduce analysis efforts
  Prune weak checks
    E.g., compare with a constant
  Remove invalid paths
    Conflicting constraints on the path
  Remove stronger accept paths
Accept paths with attacker-controlled data labelled

## Slide 16: Vulnerability analyzer
Static taint analysis
Taint engine
Pointer analysis
- Taint
- Pointer
- Tracking
- Path
Function summary
Accept path constructor
Vulnerability analyzer
Leak path constructor
Weak
accept paths
Highly-vulnerable
leakage
paths
Packet injection Vulnerabilities
Protocol states
Leak path constructor
SCC
generator
SCC

## Slide 17: Protocol state leakage analysis
Taint source:
  Protocol state
Taint sink:
  Attacker-observable channels (storage/cache/timing/…)
First check explicit information leaks
Then attacker-controlled implicit information leaks
  Track both protocol state and attacker-controlled data
  Prioritize high-entropy leakage
Trigger sink
Y
N
High
(pkt.seq > rcv_nxt)?
Low
Low
(pkt.seq == rcv_nxt)?
(pkt.seq != rcv_nxt)?

## Slide 18: Evaluation
Implemented in OCaml
  Taint analysis part: ~15K LOC
  Vulnerability analyzer: ~2.8K LOC
Analyzed 6 real code bases
  Linux kernel 3.15.8: TCP, SCTP, DCCP
  3 implementations of RTP: oRTP, PJSIP, VLC
  Target storage channel (e.g., proc file)
Tool efficiency results
  Longest: ~7.8 hours for Linux kernel TCP for taint analysis part

## Slide 19: Evaluation
Tool accuracy
  Accept path analysis
    Ground truth: all feasible accept paths
    No false negative (FN) paths
    Path pruning is effective (42.6% reduction)
  Protocol state leakage analysis
    For TCP rcv_nxt leakage
 | TP # | FP # | FN #
w/ all above (baseline) | 4 | 0 | 0
w/o field
w/o implicit flow
w/o pointer analysis
0
0
4
501
4
4
0
N/A
N/A

## Slide 20: Vulnerabilities found - TCP
For these vulnerabilities, we have implemented the attack and validated them in a controlled test bed
Linux kernel TCP
  rcv_nxt
    Find 4 high-entropy leaks
    1 reported before by manual inspection1, 3 new
  snd_nxt/una
    Most recent reported leak is fixed after Linux 3.8
    However, still find 13 high-entropy leaks , all new
    Indicate the need for an automated tool like this
232/win1
232/win2
4 high-entropy leaks (3 new)
32
1Qian et al., CCS’12
13 high-entropy leaks (all new)
32
64 packets
for a successful injection!

## Slide 21: Vulnerabilities found - RTP
3 implementations of RTP
  oRTP, PJSIP, VLC: all claim to follow RFC 3550
  Accept path analysis directly reveals vulnerability:
    oRTP, PJSIP: Only need 51 & 3 packets to inject payload
  VLC is well-protected by protocol state ssrc
    Leakage analysis: no storage channel leaks
oRTP
PJSIP
VLC
51
3
232
Inject payload:
Even these implementations follow the same RFC, their robustness against packet injection can be very different due to implementation details!

## Slide 22: Summary
PacketGuardian , an effective and scalable tool for systematic detection of packet injection vulnerability in protocol implementations
The first to propose and detect attacker-controlled implicit information leaks
  A new class of highly-exploitable implicit information leaks
Applied to 6 real code bases, and discovered new and realistic vulnerabilities on TCP, RTP, etc.
In the future, plan to improve accuracy and study more protocols
Our result website:
  http://tinyurl.com/PacketInjectionVulnerability

## Slide 23
Questions?
  http://tinyurl.com/PacketInjectionVulnerability